## Slide 1: Caches
Thus far:
  Techniques for reducing CPI by leveraging ILP
What about memory?
  Memory is significantly slower (~100x) than the processor
  If we don’t optimize, we'll have CPI close to 100!

## Slide 2: The Memory Gap
Memory subsystem design increasingly important!
H&P 6/e, Fig. 2.2
1.2x-1.5x
1.07x
Notes: Why has the speed of memory trailed behind the speed of the processor? Dennard scaling means that as transistor size decreases, it switches faster. But memory is not only logic, it involves other operations like reading the charge of memory cells and amplifying it and those steps don’t get faster as compute.

## Slide 3: Caches: Idea of a memory hierarchy
Use combination of memory kinds
  Smaller amounts of expensive but fast memory closer to the processor
  Larger amounts of cheaper but slower memory farther from the processor
Idea is not new:
“Ideally one would desire an indefinitely large memory capacity such that any particular … word would be immediately available… we are … forced to recognize the possibility of constructing a hierarchy of memories, each of which has greater capacity than the preceding but which is less quickly accessible.”
A. W. Burks, H. H. Goldstine, and J. von Neumann - 1946

## Slide 4: Why is a memory hierarchy effective?
Temporal Locality:
  A recently accessed memory location (instruction or data) is likely to be accessed again in the near future
Spatial Locality:
  Memory locations (instructions or data) close to a recently accessed location are likely to be accessed in the near future
Why does locality exist in programs?
  Instruction reuse: loops, functions
  Data working sets: arrays, temporary variables, objects
Bottom-line: small, fast caches backed up by larger, slower memories give the impression of a single, large, fast memory

## Slide 5: Memory Hierarchy
Notes: Accessing from register: 1x
Accessing from L1 cache: 3-4
L2 cache: 10-20
L3 cache: 30-80
Memory: 150 – 400
CXL memory expander: 600 – 1200 cycles
NVRAM: 3000 – 10000 cycles
Flash memory: tens of thousands of cycles
Hard disk: Millions of cycles.
Memory Level Analogy: Where You Get the Information Scaled Time
Register Reading a fact from a book open on your desk. 1 second
L1 Cache Grabbing a different book from a stack on your desk. ~3-4 seconds
L2 Cache Getting up to pull a book from a bookshelf in your office. ~10 seconds
L3 Cache Walking down the hall to a small library on your floor. ~40 seconds
Main Memory (DRAM) Taking an elevator to the main campus library in another building. ~2-3 minutes
CXL Memory Expander Getting in a car and driving to a library in the next town over. ~5-10 minutes
NVMe SSD Placing an inter-library loan request for a book from another state. ~1-2 days
Hard Disk (HDD) Requesting a rare book from an archive on another continent. ~8-12 months

## Slide 6: Memory technologies
SRAM
  Static random access memory: caches
  Uses flip flops: 6 transistors per bit
  Fast access time
  Area and power overhead per bit high
  Used for L1, L2 and L3 caches on chip
DRAM
  Dynamic random access memory: memory
  Uses typically 1 capacitor and a transistor per bit
  Slower than SRAM
  Area overhead low
  Needs to be periodically refreshed
Notes: SRAM is basically like a flip flop. 4 transistors for core logic and 2 for access. (What about register file? It is also fundamentally a bunch of flip flops, but need more ports. So lots (about a dozen) per bit. It is designed for speed but it has area of power overhead. It is volatile, meaning if power is lost, everything is lost.
A DRAM bit is essentially a capacitor (which holds a value) and a transistor (which is a gate). Because the charge can run out it needs to be periodically recharged (i.e. refreshed). Reading a bit discharges the charge so need to recharge it via a write. It is designed for density, but it slower. It is volatile because we need to refresh the charge, a power loss means data lost.

## Slide 7: Memory Technologies
Memories that have higher bandwidth
  GDDR: Used as memories for GPUs. Have wider busses, operate at a higher clock rate, tighter coupling with GPUs.
  HBM: High-bandwidth memory: stacks multiple layers of memory on top of the CPU
Flash memory
  Non-volatile
  Normally read only memory but can be erased (limit to the number of writes that can happen)
  Cheaper than DRAM but more expensive than disks
  Slower than DRAM but faster than disks
Notes: Typically, CPU is connected to DRAM via a specified interface and data flows through a bunch of pins in the cpu chip. The pins limit bandwidth. With GDDR, the memory chips are soldered on to a GPU chip and the memory circuitry also operated at a much higher clock frequency, so the effective bandwidth is much higher. HBM takes the idea even further: memory is stacked on to the processor chip for more bandwidth.
Flash memory is a transistor with an insulated floating gate. Writes are slow because a high voltage is required to force electrons through the insulator, where they become trapped; this high-voltage process also physically degrades the cell over time, leading to limited write endurance. This persistence without power makes it ideal for storage.

## Slide 8: Memory Hierarchy Issues
Block size: smallest unit that is managed at each level
  E.g., 64B for cache lines, 4KB for memory pages
Block placement: Where can a block be placed?
  E.g., direct mapped (exactly 1 location), fully associative (any location)
Block identification: How can a block be identified?
  E.g., hardware tag matching (e.g., cache), OS page table
Block replacement: Which block should be replaced?
  E.g., Random, Least recently used (LRU), Not recently used (NRU)
Write strategy: What happens on a write?
  E.g., write-through, write-back, write-allocate
Inclusivity: whether next lower level contains all the data found in the current level
  Inclusive, exclusive

## Slide 9: Cache Block Placement
Block:
0
1
12
31
Memory
Block:
0
1
2
3
4
5
6
7
Cache
Fully associative:
block 12 can go anywhere
in the cache
Block:
Cache
Set associative:
block 12 can go anywhere
in set 0
(12 mod 4)
Block:
0
1
2
3
4
5
6
7
Cache
Direct mapped:
block 12 can only go
into block 4
(12 mod 8)
Set:
0
1
2
3
4
5
6
7
0
1
2
3

## Slide 10: Summary of Cache Associativity
Fully associative
  The block from the lower level can go into any location in the cache
  Most flexible approach  lowest miss rate
  Must search the whole cache to find the block  increased access time and high power consumption
Direct mapped
  The block from the lower level can only go into one location in the cache
  Simplest approach to implement
  Blocks mapping to the same location  increased miss rates
Set associative
  Split the cache into groups of m blocks (sets)  m-way set-associative
  The block from the lower level can only go into one set, but within that set it can go anywhere
  What’s a good degree of associativity?
    Higher level caches: 2- or 4-way common
    Lower level caches: 8- to 32-way common

## Slide 11: Cache Block Identification
Every block is identified by a name or tag, which is part of the memory address
Block tag is stored alongside the block data in the cache
Block tags in the cache are compared with the tag of the requested block  often in parallel for set-associative caches, for speed
Block tag usually comprises the high-order bits of the memory address
  Data address: the address of the byte being referenced  32 bits for MIPS
  Offset: the byte within the block; e.g., 6 bits for a 64B block
  Index: the set where the block can be found; e.g., 8 bits for a 4-way 64KB cache
  Tag: the “ID” of the block; e.g., 32-8-6=18 bits
Full memory address:
Block offset
Index
Tag

## Slide 12: Address Mapping Example
Cache: 32 KBytes, 2-way, 64 byte lines
Address: 32 bits
Example: 0x000249F0 = (0000 0000 0000 0010 0100 1001 1111 0000)2

## Slide 13: Address Mapping Example
Cache: 32 KBytes, 2-way, 64 byte lines
Address: 32 bits
Example: 0x000249F0 = (0000 0000 0000 0010 0100 1001 1111 0000)2
  Byte offset
  64 bytes  6 bits  11 0000
  Index: 32K/64 = 512 lines in the cache
  512/2 = 256 sets in the cache
  256 sets  8 bits  00 1001 11 = 39
  Tag:
  0000 0000 0000 0010 01
offset
index
tag

## Slide 14: Cache Organization: Direct mapped
H&P
(2e)
Fig. 5.5 (Alpha 21064)
tag
<21>
…
?
CPU
address
Data Data
in out
valid
<1>
data
<256>
…
tag
Block address
<21>
<8>
<5>
Block
offset
Write
buffer
Lower level
memory
index

## Slide 15: Cache Organization: 2-way set associative
tag
<29>
?
CPU
address
Data Data
in out
valid
<1>
data
<512>
tag
2:1 MUX
Block address
<29>
<9>
<6>
Block
offset
Lower level
memory
index
?
H&P
Fig. 5.7
(Alpha
21264)

## Slide 16: Cache Block Replacement
To bring a new block in the cache, another block must be evicted
Direct mapped caches: there is only one choice of block to evict
Associative caches: how to choose a “victim”?
  Random: select a victim block in the set randomly
  Least-recently-used (LRU): select the block that has not been used for the longest period of time  works well in practice because of the principle of locality
  Not-recently-used (NRU): select a block other than the most-recently used block.
    Need less storage than LRU and performs better than random
  Ideal: select the block that will not be used for the longest period of time  requires knowledge of the future  unrealistic!

## Slide 17: Cache Write Strategies
How are the writes handled (i.e, when do stores reach a lower level of the memory hierarchy)?
Write through: write to lower level as cache is modified
  Writes will perform at the speed of the lower level of memory hierarchy
  Generates more traffic
  Lower level is kept coherent with higher level (particularly important for multi-processors)
Write back: only write to lower level when the block is evicted
  Writes will perform at the speed of the higher level
  Generates less traffic
  Lower level can have stale data for some time (cache-coherency problem)

## Slide 18: Cache Write Strategies
What happens if the block is not found in the cache?
Write allocate: bring the block into the cache and write to it
  Good if block will soon be used by another memory access (locality)
  Usually used with write back
Write no-allocate: do not bring block into cache and modify data in the lower level
  Good if no memory access to the same block occur in the near future
  Usually used with write through

## Slide 19: Multi-Level Caches
Do lower-level caches keep a copy of the block that’s brought into a higher-level cache?
Inclusive caches:
  Lower-level cache has a copy of every block in higher-level caches
  Wastes capacity of lower-level caches 
  Simplifies finding a cache block by another entity (e.g., by other processors) 
Exclusive caches:
  A block may reside in only one level of the cache hierarchy
  Maximizes aggregate capacity of the cache hierarchy 
  Requires a uniform block size for all cache levels 