## Slide 1: Cache Performance
Memory system and processor performance:
Improving memory hierarchy performance:
  Decrease hit time
  Decrease miss rate
  Decrease miss penalty
CPU time = IC x CPI x Clock time
CPI = CPIld/st x + CPIothers x
IC
ICld/st
IC
ICothers
CPIld/st = Average memory access time (AMAT)
AMAT= Hit time + Miss rate x Miss penalty
CPU performance eqn.
Memory performance eqn.

## Slide 2: Cache Performance – example problem
Assume we have a computer where the CPI is 1 when all memory accesses hit in the cache. Data accesses (ld/st) represent 50% of all instructions. If the miss penalty is 25 clocks and the miss rate is 2%, how much faster would the computer be if all instructions were cache hits?
[H&P 5th ed, B.1]

## Slide 4: Reducing Cache Miss Rates
Cache miss classification: the “three C’s”
Compulsory misses (or cold misses): when a block is accessed for the first time
Capacity misses: when a block is not in the cache because it was evicted because the cache was full
Conflict misses: when a block is not in the cache because it was evicted because the cache set was full
  Conflict misses only exist in direct-mapped or set-associative caches
  In a fully associative cache, all non-compulsory misses are capacity misses

## Slide 5: Cache Misses vs. Cache Size
H&P
Fig. 5.15
Direct mapped
4-way set associative
Miss rates are very small in practice (caching is effective!)
Miss rates decrease significantly with cache size
  Rule of thumb: miss rates change in proportion to √ of cache size e.g., 2x cache  √2 fewer misses
Miss rates decrease with set-associativity because of reduction in conflict misses
Notes: Sqrt 2 = 1.4

## Slide 6: Reducing Cold Miss Rates
Technique 1: Large block size
  Principle of spatial locality  other data in the block likely to be used soon
  Reduce cold miss rate
  May increase conflict and capacity miss rate for the same cache size (fewer blocks in cache)
  Increase miss penalty because more data has to be brought in each time
  Uses more memory bandwidth
Notes: Why does too large a block size increase conflict misses? Because the probability of conflicts increases with a large block size.
It increases capacity misses because of increased cache pollution.

## Slide 7: Cache Misses vs. Block Size
Small caches are very sensitive to block size
Very large blocks (> 128B) never beneficial
64B is a sweet spot  common choice in today’s processors
H&P
Fig. 5.16

## Slide 8: Reducing Cold Miss Rates
Technique 2: Prefetching
  Idea: bring into the cache ahead of time data or instructions that are likely to be used soon
  Can reduce cold misses (also capacity misses)
  Uses more memory bandwidth
  Does not typically increase miss penalty (prefetch is generally handled after main cache access is completed)
  May increase conflict and capacity miss rates by displacing useful blocks (cache pollution)
    Can use a prefetch buffer to avoid polluting the cache

## Slide 9: Prefetching
Hardware prefetching: hardware automatically prefetches cache blocks on a cache miss
  No need for extra prefetching instructions in the program
  Effective for regular accesses, such as instructions
  E.g., next blocks prefetching, stride prefetching
Software prefetching: compiler inserts instructions at proper places in the code to trigger prefetches
  Requires ISA support (nonbinding prefetch instruction)
  Adds instructions to compute the prefetching addresses and to perform the prefetch itself (prefetch overhead)
  E.g., data prefetching in loops, linked list prefetching

## Slide 10: Software Prefetching
E.g., prefetching in loops: Brings the next required block, two iterations ahead of time (assuming each element of x is 4-bytes long and the block has 64 bytes).
E.g, linked-list prefetching: Brings the next object in the list
for (i=0; i<=999; i++) {
if (i%16 == 0)
prefetch(x[i+32]);
x[i] = x[i] + s;
}
for (i=0; i<=999; i++) {
x[i] = x[i] + s;
}
while (student) {
student->mark = rand();
student = student->next;
}
while (student) {
prefetch(student->next);
student->mark = rand();
student=student->next;
}

## Slide 11: Reducing Conflict Miss Rates
Technique 3: High associativity caches
  More options for block placement  fewer conflicts
  Reduce conflict miss rate
  May increase access (hit) time because tag match takes longer
  May increase miss penalty because replacement policy is more involved

## Slide 12: Cache Misses vs. Associativity
Small caches are very sensitive to associativity
In all cases more associativity decreases miss rate, but little difference between 4-way and fully associative (unless huge cache)

## Slide 13: Reducing Miss Rates
Technique 4: Compiler optimizations
  E.g., merging arrays: may improve spatial locality if the fields are used together for the same index
  E.g., loop fusion: improves temporal locality
int val[size];
int key[size];
struct valkey{
int val;
int key;
};
Struct valkey merged_array[size];
for (i=0; i<1000; i++)
A[i] = A[i]+1;
for (i=0; i<1000; i++)
B[i] = B[i]+A[i];
for (i=0; i<1000; i++) {
A[i] = A[i]+1;
B[i] = B[i]+A[i];
}
Notes: Merging arrays: NOT beneficial of walking through every array element (spatial locality will cover both arrays). Very beneficial for random accesses

## Slide 14: Reducing Miss Rates
  E.g., blocking: change row-major and column-major array distributions to block distribution to improve spatial and temporal locality
for (i=0; i<5; i++)
for (j=0; j<5; j++) {
r=0;
for (k=0; k<5; k++) {
r=r+y[i][k]*z[k][j];
x[i][j]=r;
}
// matrix multiplication
i=0;j=0;0<k<5
i=0;j=1;0<k<5
x:
y:
z:
i=1;j=0;0<k<5
…
Poor spatial and temporal locality
Poor temporal locality

## Slide 15: Reducing Miss Rates – Loop Blocking or Tiling
for (jj = 0; jj < 5; jj = jj+2)
for (kk = 0; kk < 5; kk = kk+2)
for (i = 0; i < 5; i++)
for (j = jj; j < min(jj+2-1,5); j++)
{ r = 0;
for (k = kk; k < min(kk+2-1,5); k++)
r = r + y[i][k]*z[k][j];
x[i][j]= x[i][j] + r;
}
jj=0;kk=0;i=0;j=0;0<k<1
jj=0;kk=0;i=0;j=1;0<k<1
x:
y:
z:
jj=0;kk=0;i=1;j=0;0<k<1
Better temporal locality
Notes: For full details, see H & P, 4/e, pages 302-305.

## Slide 16: Cache Performance II
Memory system and processor performance:
Improving memory hierarchy performance:
  Decrease hit time
  Decrease miss rate (block size, prefetching, associativity, compiler)
  Decrease miss penalty
CPU time = IC x CPI x Clock time
Avg. mem. time = Hit time + Miss rate x Miss penalty
CPU performance eqn.
Memory performance eqn.

## Slide 17: Reducing Cache Miss Penalty
Technique 1: Victim caches
  (Can also be considered to reduce miss rate)
  Very small cache used to capture evicted lines from cache
    Targets conflict misses
  In case of cache miss the data may be found quickly in the victim cache
  Typically 8-32 entries, fully-associative
  Access victim cache in series or in parallel with main cache: trade-off?
CPU
L1 cache
tag
data
Victim cache
tag
data
?
Memory address
?
Main
memory

## Slide 18: Reducing Cache Miss Penalty
Technique 2: giving priority to reads over writes
  The value of a a load is likely to be used soon (i.e., dependent inst may stall), while writes are “fire-and-forget”
    Insight: writes are “off the critical path” and their latency doesn’t usually matter. Thus, don’t stall for writes!
  Idea: place write misses in a write buffer, and let read misses overtake writes
    Flush the writes from the write buffer when pipeline is idle or when buffer full
  Reads to the memory address of a pending write in the buffer now become hits in the buffer:
1. write miss goes
into write buffer
sw 512(r0), r3
…
lw r2, 512(0)
2. read hits in the write buffer
and gets the value from the
previous write
memory
address
value
512
R[r3]
…
…
…
…
write buffer
Notes: Reduces hit time too!

## Slide 19: Reducing Cache Miss Penalty
Technique 3: early restart and critical word first
  On a read miss, processor needs just the requested word (or byte)
    but processor must wait until the whole block is brought into the cache
  Early restart: as soon as the requested word arrives in the cache, send it to the processor
    Meanwhile, continue reading the rest of the block into the cache
CPU
L1 cache
tag
data
?
Main
memory
lw r2, 3(0)
0x0003
01
02
03
Cache block
00
03
04 … 05 … 06 …

## Slide 20: Reducing Cache Miss Penalty
Technique 3: early restart and critical word first
  On a read miss, processor needs just the requested word (or byte)
    but processor must wait until the whole block is brought into the cache
  Critical word first: get the requested word first from the memory and immediately send it to the processor
    Meanwhile, continue reading the rest of the block into the cache
CPU
L1 cache
tag
data
?
Main
memory
lw r2, 3(0)
0x0003
03
Cache block
03
00 … 01 … 02 … 04 …

## Slide 21: Reducing Cache Miss Penalty
Technique 4: non-blocking (or lockup-free) caches
  Non-blocking caches: other memory instructions can overtake a cache miss instruction
    Cache can service multiple hits while waiting on a miss: “hit under miss”
    More aggressive: cache can service multiple hits while waiting on multiple misses: “miss under miss” or “hit under multiple misses”
  Cache and memory must be able to service multiple requests concurrently
    Particularly valuable in dynamically scheduled (out-of-order) processors
  Must keep track of multiple outstanding memory operations
    New hardware structure: Miss Status Handler Registers (MSHRs)
      Address of a block being waited on
      Capability to merge multiple requests to the same block
      Destination register

## Slide 22: Non-blocking Caches
H&P
Fig. 5.23
Significant improvement from small degree of outstanding memory operations
Some applications benefit from large degrees

## Slide 23: Reducing Cache Miss Penalty
Technique 5: second level caches (L2)
  Gap between main memory and L1 cache speeds is increasing
  L2 makes main memory appear to be faster if it captures most of the L1 cache misses
    L1 miss penalty becomes L2 hit access time if hit in L2
    L1 miss penalty higher if miss in L2
  L2 considerations:
    256KB – 4MB capacity (last level of cache in smartphones & tablets)
    ~10-20 cycles access time
    Higher associativity (e.g., 8-16 ways) possible. Why?
    Higher miss rate than L1. Why?
  L3 caches are common on laptop/desktop/server processors
    30+ cycle access time
    2-20+ MB capacity
    Very high associativity (16-32 ways)

## Slide 24: Second Level Caches
Memory subsystem performance:
Miss rates:
  Local: the number of misses divided by the number of requests to the cache
    E.g., Miss rateL1 and Miss rateL2 in the equations above
    Usually not so small for lower level caches
  Global: the number of misses divided by the total number of requests from the CPU
    E.g, L2 global miss rate = Miss rateL1 x Miss rateL2
    Represents the aggregate effectiveness of the cache hierarchy
Avg. mem. time = Hit timeL1 + Miss rateL1 x Miss penaltyL1
Miss penaltyL1 = Hit timeL2 + Miss rateL2 x Miss penaltyL2
 Avg. mem. time = Hit timeL1 + Miss rateL1 x (Hit timeL2 + Miss rateL2 x Miss penaltyL2)

## Slide 25: Cache Misses vs. L2 size
L2 caches must be much bigger than L1
Local miss rates for L2 are larger than for L1 and are not a good measure of overall performance
H&P
Fig. 5.10
Secondary working set accommodated

## Slide 26: Cache Performance II
Memory system and processor performance:
Improving memory hierarchy performance:
  Decrease hit time
  Decrease miss rate (block size, prefetching, associativity, compiler)
  Decrease miss penalty (victim caches, reads over writes, prioritize critical word, non-blocking caches, additional cache levels)
CPU time = IC x CPI x Clock time
Avg. mem. time = Hit time + Miss rate x Miss penalty
CPU performance eqn.
Memory performance eqn.

## Slide 27: Reducing Cache Hit Time
Technique 1: small and simple caches
  Small caches are compact  have short wire spans
    Wires are slow
  Low associativity caches have few tags to compare against the requested data
  Direct mapped caches have only one tag to compare and comparison can be done in parallel with the fetch of the data

## Slide 28: Reducing Cache Hit Time
Technique 2: virtual address caches
  Programs use virtual addresses for data, while main memory uses physical addresses  addresses from processor must be translated at some point
  Option 1: physical address caches  perform address translation before cache access
    Hit time is increased to accommodate translation
CPU
L1 cache
tag
data
?
Main
memory
0x0003
address
translation
0x2103

## Slide 29: Reducing Cache Hit Time
Technique 2: virtual address caches
  Option 2: virtual address caches  perform address translation after cache access if miss
    Hit time does not include translation
CPU
L1 cache
tag
data
?
Main
memory
0x0003
address
translation
0x2103

## Slide 30: Cache Performance Techniques
technique | miss rate | miss penalty | hit time | complexity
large block size | J | L |  | J
high associativity | J |  | L | L
victim cache | J | J |  | L
hardware prefetch | J |  |  | L
compiler prefetch | J |  |  | L
compiler optimizations | J |  |  | L
prioritisation of reads |  | J |  | L
critical word first |  | J |  | L
nonblocking caches |  | J |  | L
L2 caches |  | J |  | L
small and simple caches | L |  | J | J
virtual-addressed caches |  |  | J | L