## Slide 1: End of the Uniprocessor?
Frequency has stopped scaling : Power Wall
  End of Dennard scaling
Memory wall
  Instructions and data must be fetched
  Memory becomes the bottleneck
ILP Wall
  Dependencies between instruction limit ILP
CS/ECE 6810 Computer Architecture
End of performance scaling for uniprocessors has forced industry to turn to chip-multiprocessors (Multicores)
Notes: Frequency has stopped scaling due to the breakdown of Dennard scaling. One of the important corollaries of Moore’s law was Dennard scaling which said that as the size of the transistor shrinked, the clocked faster, and consumed approximately the same power in unit area.
But that broken in the mid 2000s because of power dissipation issues. So supply voltage had to be reduced which meant frequency stagnated.

## Slide 2: Shared Memory Multiprocessors
CS/ECE 6810 Computer Architecture
Obtained by connecting full processors together
  Processors have their own connection to memory
  Processors are capable of independent execution and control
Have a single OS for the whole system, support both processes and threads, and appear as a common multiprogrammed system
  (Thus, by this definition, Beowulf clusters are not multiprocessors)
Can be used to run multiple sequential programs concurrently or parallel programs
Suitable for parallel programs where threads can follow different code (task-level-parallelism)

## Slide 3: Shared Memory Multiprocessors
CS/ECE 6810 Computer Architecture
Two common organizations:
  Physically centralized memory, uniform memory access (UMA) (a.k.a. SMP)
  Physically distributed memory, non-uniform memory access (NUMA)
  (Note: both organizations have local caches)
CPU
Main memory
CPU
CPU
CPU
Cache
Cache
Cache
Cache
CPU
Mem.
CPU
CPU
CPU
Cache
Cache
Cache
Cache
Mem.
Mem.
Mem.

## Slide 4: Modern Multicore Processor
CS/ECE 6810 Computer Architecture
Notes: Modern multicore processors are complex entities and have aspects of “UMA” and “NUMA”. The picture above shows a dual-socket (chip) multiprocessor. With respect to the cores 0 through 4, accessing local memory is has roughly the same latency. But for these cores to access the other socket, latencies are significantly higher.

## Slide 5: Shared Memory Multiprocessors
CS/ECE 6810 Computer Architecture
The communication model:
  Threads in different processors can use the same virtual address space
  Communication is done through shared memory variables
data = 10;
x = data * y;
Producer (p1)
Consumer (p2)

## Slide 6: Shared Memory Multiprocessors
CS/ECE 6810 Computer Architecture
Recall the communication model:
  Threads in different processors can use the same virtual address space
  Communication is done through shared memory variables
  Explicit synchronization (e.g., variable flag below)
flag = 0;
…
data = 10;
flag = 1;
flag = 0;
…
while (!flag);
x = data * y;
Producer (p1)
Consumer (p2)

## Slide 7: HW Support for Shared Memory
Cache Coherence
  Caches + multiprocessers  stale values
  System must behave as if caches are not present
  Cache coherence is implementation that ensures this via:
    Write propagation
    Write serialization
Memory Consistency
  When (in what order) should writes propagate?
  What value should a read return?
  Memory consistency is a specification.
Primitive synchronization instructions
  Certain hardware instructions are extremely useful/required for achieving synchronisation
  Memory fences: memory ordering on demand
  Read-Modify-writes: support for locks (critical sections)
  Transactional memory extensions
CS/ECE 6810 Computer Architecture
Notes: Illusion of shared memory implies 3 things.
- cache coherence. Keep caches consistent.
- once caches kept consistent. In what order writes are propagated. Consistency.
- Primitive synchronization.

## Slide 8: Cache Coherence
CS/ECE 6810 Computer Architecture
flag = 0;
…
data = 10;
flag = 1;
flag = 0;
…
while (!flag);
x = data * y;
Producer (p1)
Consumer (p2)
The update to flag (and data) should be (eventually) visible to p2

## Slide 9: Cache Coherence
CS/ECE 6810 Computer Architecture
CPU
Main memory
CPU
CPU
CPU
Cache
Cache
Cache
Cache
CPU
Main memory
CPU
CPU
CPU
Make Caches Invisible!

## Slide 10: Memory Consistency
CS/ECE 6810 Computer Architecture
flag = 0;
…
data = 10;
flag = 1;
flag = 0;
…
while (!flag) {}
x = data * y;
Producer (p1)
Consumer (p2)
If p2 sees the update to flag, will p2 see the update to data?

## Slide 11: Primitive Synchronization
CS/ECE 6810 Computer Architecture
flag = 0;
…
data = 10;
flag = 1;
flag = 0;
…
while (!flag) {}
x = data * y;
Producer (p1)
Consumer (p2)
If p2 sees the update to flag, will it see the update to data?
fence
fence

## Slide 12: The Cache Coherence Problem
CS/ECE 6810 Computer Architecture
CPU
Main memory
CPU
CPU
Cache
Cache
Cache
T0: A=1
T0: A not cached
T0: A not cached
T0: A not cached
T1: load A (A=1)
T1: A=1
T1: A not cached
T1: A not cached
T2: load A (A=1)
T2: A not cached
T2: A=1
T2: A=1
T3: store A (A=2)
T3: A not cached
T3: A=1
T3: A=1
stale
stale
T4: load A (A=1)
T4: A=1
T4: A=2
T4: A=1
use old value
T5: load A (A=1)
use stale value!

## Slide 13: Cache Coherence
Write Propagation
  writes are (eventually) visible in all processors
Write Serialization
  Writes are observable in the same order from all processors
CS/ECE 6810 Computer Architecture
// Initially all values are 0.
P1 P2 P3 P4
X= 1 X=2
=X(1) =X(2)
=X(2) =X(1)
Notes: These are two necessary (but not sufficient) conditions for cache coherence. Intuitively, the system must behave as if caches are invisible.
Write propagation. A store performed by one processor must be eventually visible to a load reading from the same address at another processor. Note that without caches, write propagation happens though memory.
The second condition is called write serialization. Basically all processors should agree on the order of the writes to the same address. This again is true when there are no caches. The order in which the writes are serialized is the order in which writes reach memory, and this is the order in which they are observed by all processors. But in the presence of caches, and if we are not careful about the order in which writes are propagated, this can be violated. For example, in the example shown it is possible for the write from P1 to reach P2 before P3, and vice versa for the write from P4.

## Slide 14: Cache Coherence Protocols
CS/ECE 6810 Computer Architecture
Idea of most protocols:
  Keep track of what processors have copies of what data
  Enforce at any given time a single value of every data exists:
    By getting rid of data with old values → invalidate protocols
    By updating everyone’s copy of the data → update protocols
  They enforce the Single-Writer-Multiple-Reader Invariant (or SWMR).
There are two alternating epochs: A single writer epoch, a multiple reader epoch
Before a write happens, it must communicate with all other actors to obtain exclusive access.
CPU
Main memory
CPU
CPU
CPU
Cache
Cache
Cache
Cache
CPU
Main memory
CPU
CPU
CPU
Notes: Key insight: ok to have multiple cached copies as long as the values are all the same.
Whenever a store, that is a write, happens in a cache – it needs to communicate with the other cached copies by either invalidating the other cache copies are updating the values of the other cached copies.

## Slide 15: Cache Coherence Protocols
CS/ECE 6810 Computer Architecture
Idea of most protocols:
  Keep track of what processors have copies of what data
  Enforce that at any given time a single value of every data exists:
    By getting rid of copies of the data with old values → invalidate protocols
    By updating everyone’s copy of the data → update protocols
  They enforce the Single-Writer-Multiple-Reader Invariant (or SWMR).
SWMR:
  Guarantee that old values are eventually invalidated/updated (write propagation)
  Guarantee that only a single processor is allowed to modify a certain datum at any given time (write serialization)
CPU
Main memory
CPU
CPU
CPU
Cache
Cache
Cache
Cache
CPU
Main memory
CPU
CPU
CPU

## Slide 16: Write-invalidate Example
CS/ECE 6810 Computer Architecture
CPU
Main memory
CPU
CPU
Cache
Cache
Cache
T1: load A (A=1)
T1: A=1
T1: A not cached
T1: A not cached
T2: load A (A=1)
T2: A not cached
T2: A=1
T2: A=1
T3: store A (A=2)
T3: A not cached
T3: A not cached
T3: A=1
invalidate
stale
T4: load A (A=2)
T4: A not cached
T4: A=2
T4: A=2
new value
T5: load A (A=2)
new value

## Slide 17: Write-update Example
CS/ECE 6810 Computer Architecture
CPU
Main memory
CPU
CPU
Cache
Cache
Cache
T1: load A (A=1)
T1: A=1
T1: A not cached
T1: A not cached
T2: load A (A=1)
T2: A not cached
T2: A=1
T2: A=1
T3: store A (A=2)
T3: A not cached
T3: A = 2
T3: A=2
update
update
T4: load A (A=2)
T4: A = 2
T4: A=2
T4: A=2
new value
T5: load A (A=2)

## Slide 18: Invalidate vs. Update Protocols
CS/ECE 6810 Computer Architecture
Invalidate:
  + Multiple writes by the same processor to the cache block only require one invalidation
  + No need to send the new value of the data (less bandwidth)
  Caches must be able to provide up-to-date data upon request
  Must write-back data to memory when evicting a modified block
  Usually used with write-back caches (more popular)
Update:
  + New value can be re-used without the need to ask for it again
  + Data can always be read from memory
  + Modified blocks can be evicted from caches silently
  Possible multiple useless updates (more bandwidth)
  Usually used with write-through caches (less popular)

## Slide 19: Cache Coherence Protocols
CS/ECE 6810 Computer Architecture
Implementation can either be in software or hardware.
Software coherence: Programmer-directed or compiler-controlled
  Expose instructions such as writeback and self-invalidate to software
  Insert these at appropriate points, e.g., by leveraging static analysis.
  Problem: conservatism of static analysis (or programmer burden)
Hardware coherence
  Add state bits to cache lines to track state of the line
    Most common: Modified, Owned, Exclusive, Shared, Invalid
    Protocols usually named after the states supported
  Cache lines transition between states upon load/store operations from the local processor and by remote processors
  These state transitions must guarantee SWMR and in doing so:
    write propagation and
    write serialization
Notes: The goal is to enforce SWMR by exchanging as few messages as possible.

## Slide 20: Example: MSI Protocol
CS/ECE 6810 Computer Architecture
States:
  Modified (M): block is cached only in this cache and has been modified
  Shared (S): block is cached in this cache and possibly in other caches (no cache can modify the block)
  Invalid (I): block is not cached

## Slide 21: Example: MSI Protocol
CS/ECE 6810 Computer Architecture
Transactions originated at this CPU:
Invalid
Shared
Modified
CPU read miss
CPU read hit
CPU write miss
CPU write (upgrade)
CPU write hit
CPU read hit

## Slide 22: Example: MSI Protocol
CS/ECE 6810 Computer Architecture
Transactions originated at other CPU:
Invalid
Shared
Modified
CPU read miss
CPU read hit
CPU write miss
CPU write
CPU write hit
CPU read hit
Remote write miss
Remote write miss
Remote read miss
Remote read miss

## Slide 23: Example: MESI Protocol
CS/ECE 6810 Computer Architecture
States:
  Modified (M): block is cached only in this cache and has been modified
  Exclusive (E): block is cached only in this cache, has not been modified, but can be modified at will
  Shared (S): block is cached in this cache and possibly in other caches
  Invalid (I): block is not cached
State E is obtained on reads when no other processor has a shared copy
  All processors must answer if they have copies or not
  Or some device must know if processors have copies
Advantage over MSI
  Often variables are loaded, modified in register, and then stored
  The store on state E then does not require asking for permission to write

## Slide 24: Example: MESI Protocol
CS/ECE 6810 Computer Architecture
Transactions originated at this CPU:
Invalid
Shared
Modified
CPU read miss & sharing
CPU read hit
CPU write miss
CPU write
CPU write hit
CPU read hit
Exclusive
CPU read hit
CPU read miss & no sharing
CPU write
Must inform everyone
(upgrade)
Can be done silently

## Slide 25: Example: MESI Protocol
CS/ECE 6810 Computer Architecture
Transactions originated at other CPU:
Invalid
Shared
Modified
Exclusive
Remote write
miss
Remote read miss
Remote write miss
Remote read miss
Remote read miss
Remote write miss

## Slide 26: Behavior of Cache Coherence Protocols
CS/ECE 6810 Computer Architecture
Uniprocessor cache misses (the 3 C’s):
  Cold (or compulsory) misses: when a block is accessed for the first time
  Capacity misses: when a block is not in the cache because it was evicted because the cache was full
  Conflict misses: when a block is not in the cache because it was evicted because the cache set was full
Coherence misses: when a block is not in the cache because it was invalidated by a write from another processor
  Hard to reduce ® relates to intrinsic communication and sharing of data in the parallel application
  False sharing coherence misses: processors modify different words of the cache block (no real communication or sharing) but end up invalidating the complete block

## Slide 27: Behavior of Cache Coherence Protocols
CS/ECE 6810 Computer Architecture
False sharing misses increases with larger cache line size
  Only true sharing remains with single word/byte cache lines
False sharing misses can be reduced with better placement of data in memory
True sharing misses tends to decrease with larger cache line sizes (due to locality)
Classifying misses in a multiprocessor is not straightforward
  E.g., if P0 has line A in the cache and evicts it due to capacity limitation, and later P1 writes to the same line: is this a capacity or a coherence miss?
  It is both, as fixing one problem (e.g., increasing cache size) won’t fix the other

## Slide 28: Behavior of Cache Coherence Protocols
CS/ECE 6810 Computer Architecture
Common types of data access patterns
  Private: data that is only accessed by a single processor
  Read-only shared: data that is accessed by multiple processors but only for reading (this includes instructions)
  Migratory: data that is used and modified by multiple processors, but in turns
  Producer-consumer: data that is updated by one processor and consumed by another
  Read-write: data that is used and modified by multiple processors simultaneously
    Data used for synchronization
Bottom-line: threads don’t usually read and write the same data indiscriminately

## Slide 29: Possible Implementations
CS/ECE 6810 Computer Architecture
Two ways of implementing coherence protocols in hardware
  Snooping: all cache controllers monitor all other caches’ activities and maintain the state of their lines
    Commonly used with buses and in many CMP’s today
  Directory: a central control device directly handles all cache activities and tells the caches what transitions to make
    Can be of two types: physically centralized and physically distributed
    Commonly used with scalable interconnects and in many CMP’s today