## Slide 1: Lect. 12: Coherence Protocols
CS/ECE 6810 Computer Architecture
Snooping coherence
Directory coherence

## Slide 2: Snooping Coherence Protocol
CS/ECE 6810 Computer Architecture
Snooping coherence on simple shared bus
  “Easy” as all processors and memory controller can observe all transactions
  Bus-side cache controller monitors the tags of the lines involved and reacts if necessary by checking the contents and state of the local cache
  Bus provides a serialization point (i.e., any transaction A is either before or after another transaction B)
    More complex with split transaction buses
P1
L1
0
0
Line state
P2
L1
0
0
Line state
Cache states:
00 = invalid
01 = shared
10 = modified

## Slide 3: Snooping on a simple bus
CS/ECE 6810 Computer Architecture
Read/Write miss
  When should memory provide data?
    Wait until inhibit is deasserted
    If Wired OR (sharers, modified) is false, then provides data.
  Write-backs?
    Don’t want to wait for writes  Write-back buffer
P1
L1
0
0
Line state
P2
L1
0
0
Line state
Cache states:
00 = invalid
01 = shared
10 = modified

## Slide 4: Snooping on Simple Bus
CS/ECE 6810 Computer Architecture
“The devil is in the details”, Classic Proverb
Problem: conflict when processor and bus-side controller must check the cache
Solutions:
  Use dual-ported modules for the tag and state array
  Or, duplicate tag and state array
    Both must be kept consistent when one is changed
P1
L1
0
0
Line state
P2
L1
0
0
Line state
Cache states:
00 = invalid
01 = shared
10 = modified
Ld/St

## Slide 5: Snooping on Simple Bus
CS/ECE 6810 Computer Architecture
Fig 6.4
Culler et al.

## Slide 6: Snooping on Simple Bus
CS/ECE 6810 Computer Architecture
Problem: even if bus is atomic, state transitions are not instantaneous and may require several steps → transitions are not atomic
  E.g., read- miss transaction = wait for bus + [wait for bus-side controllers to check cache + data response (or memory response)]
  E.g. write-upgrade transactions = wait for bus + [wait for bus-side controllers to invalidate]
What to do if there are conflicting requests on the bus to same cache line?

## Slide 7: Snooping on Simple Bus
CS/ECE 6810 Computer Architecture
What to do if there are conflicting requests on the bus to same cache line?
  Suppose to processors with local caches for a block in state S
  Both of them want to write, which is an upgrade transaction
    Upgrade transaction waits for the bus; then sends invalidation messages and once that is complete; the write happens.
  How do we deal with this race condition?

## Slide 8: Snooping on Simple Bus
CS/ECE 6810 Computer Architecture
How do we deal with the race condition?
  The winning bus transaction invalidates the cache line of the loser cache
  What should the loser cache now do? Cannot simply issue an updrade. Must now issue a write miss.
  In other words, race conditions like these need to be caught and dealt with correctly.

## Slide 9: Snooping on Simple Bus
CS/ECE 6810 Computer Architecture
Problem: even if bus is atomic, state transitions are not instantaneous and may require several steps → transitions are not atomic
  E.g., read- miss transaction = wait for bus + [wait for bus-side controllers to check cache + data response (or memory response)]
  E.g. write-upgrade transactions = wait for bus + [wait for bus-side controllers to invalidate]
What to do if there are conflicting requests on the bus to same cache line?
  E.g., an upgrade request may lose bus arbitration to another processor’s and may have to be re-issued as a full write miss (due to the intervening invalidation)
Solution:
  Introduce transient states to cache lines and the protocol (the I, S, M, etc states seen in Lecture 3 are then called the stable states)

## Slide 10: Example: Extended MESI Protocol
CS/ECE 6810 Computer Architecture
Transactions originating at this CPU:
Invalid
Shared
Modified
CPU write miss
CPU write
CPU write hit
CPU read hit
Exclusive
CPU read hit
CPU read miss & shr.
CPU read miss & no shr.
CPU write
I→S,E
CPU read hit
I→M
S→M
CPU write miss
bus granted
CPU read
bus granted & shr.
bus granted & no shr.
CPU write
bus granted
& no conflict
conflict

## Slide 11: Snooping with Multi-Level Hierarchies
CS/ECE 6810 Computer Architecture
Problems:
  Processor interacts with L1 while bus snooping device interacts with L2, and propagating such operations up or down is not instantaneous
P1
L1
0
0
Line state
P2
L1
0
0
Line state
Cache states:
00 = invalid
01 = shared
10 = modified
Ld/St
L2
0
0
Line state
L2
0
0
Line state

## Slide 12: Snooping with Multi-Level Hierarchies
CS/ECE 6810 Computer Architecture
Solution:
1. Maintain inclusion property
  Lines in L1 must also be in L2 → no data is found solely in L1, so no risk of missing a relevant transaction when snooping at L2
  Lines in M state in L1 must also be in M state in L2→ snooping controller at L2 can identify all data that is modified locally
2. Propagate coherence transactions to L1 as well.
    Propagate all bus transactions from to L1, whether relevant or not
    Keep extra state in the L2 lines to tell whether the line is also present in L1 or not (inclusion bits). If it is present in L2, but inclusion bits say it is not present in L1, no need to propagate transaction to L1.

## Slide 13: Snooping with Multi-Level Hierarchies
CS/ECE 6810 Computer Architecture
Maintaining inclusion property
Assume: L1: associativity a1, number of sets n1, block size b1
L2: associativity a2, number of sets n2, block size b2
  Difficulty: Replacement policy (e.g., LRU)
  Assume: a1=a2=2; b1=b2; n2=k*n1; lines m1, m2, and m3 map to same set in L1 and the same set in L2; initially m1 is present in L1 and L2
m1
L1
m1
L2
P
miss m2
2
Miss m2
3
Ld m2
1
m2
m2
Fill m2
4
Fill m2
5
Miss m3
8
Miss m3
9
Ld m1
6
hit
Ld m3
7
Fill m3
10
Fill m3
11
m3
m3
Problem: m1 is L1 but not in L2!!!

## Slide 14: Snooping with Multi-Level Hierarchies
CS/ECE 6810 Computer Architecture
Maintaining inclusion property
Assume: L1: associativity a1, number of sets n1, block size b1
L2: associativity a2, number of sets n2, block size b2
  Difficulty: Different line sizes
  Assume: a1=a2=1; b1=1, b2=2; n1=4, n2=8
  Thus, words w0 and w17 can coexist in L1, but not in L2
w0
L1
L2
w1
w2
w3
w16
w17

## Slide 15: Snooping with Multi-Level Hierarchies
CS/ECE 6810 Computer Architecture
Maintaining inclusion property
  Most combinations of L1/L2 size, associativity, and line size do not automatically lead to inclusion
  Static solution: One solution is to have a1=1, a2≥1, b1=b2, and n1≤n2
  Dynamic solution: More common solution is to invalidate the L1 line (or lines, if b1<b2) upon replacing a line in L2. Must also invalidate L1 line(s) when L2 line is invalidated due to coherence
    Propagate all invalidations from L2 to L1, whether relevant or not
    Keep extra state in the L2 lines to tell whether the line is also present in L1 or not (inclusion bits)
  Finally, add a new state to L2 (modified-but-stale) to keep track of lines that are in state M in L1 (or make L1 write-through)

## Slide 16: Snooping with Split-Transaction Buses
CS/ECE 6810 Computer Architecture
Non-split-transaction buses are idle from when the address request is finished until the data returns from memory or another cache
In split-transaction buses transactions are split into a request transaction and a response transaction, which can be separated
Sometimes implemented as two buses: one for requests and one for responses
Address
(normal)
address 1
address 2
address 2
Data
(normal)
data 1
Address
(split)
address 1
address 3
Data
(split)
data 0
data 1

## Slide 17: Snooping with Split-Transaction Buses
CS/ECE 6810 Computer Architecture
Problems
  Multiple requests can clash (e.g., a read and a write, or two writes, to the same data) (Note that this is more complicated than the case in Slide 4, as now different transactions may be at different stages of service)
  Buffers used to hold pending transactions may fill up (flow control is required)
  Responses from multiple requests may appear in a different order than their respective requests
    Responses and requests must then be matched using tags for each transaction

## Slide 18: Snooping with Split-Transaction Buses
CS/ECE 6810 Computer Architecture
Clashing requests
  snoop controllers keep track themselves of what transactions are pending, in case there is conflict
  Allow only one request at a time for each line (e.g., SGI Challenge)
Flow control
  Use negative acknowledgement (NACK) when buffers are full (requests must be retried later; a bit more tricky with responses, due to danger of deadlock) (e.g., SGI Challenge)
  Or, design the size of all queues for the worst case scenario
Ordering of transactions
  Responses can appear in any order → the interleaving of the requests fully determine the order of transactions (e.g., SGI Challenge)
  Or, enforce a FIFO order of transactions across the whole system (caches + memory) (e.g., Sun Enterprise)

## Slide 19: Snooping with Ring
CS/ECE 6810 Computer Architecture
Like a bus, rings easily support broadcasts
Snooping implemented by all controllers checking the message as it passes by and re-injecting it into the ring
Potentially multiple transactions can be simultaneously on different stretches of the ring (harder to enforce proper ordering)
Large latency for long rings and growing linearly with number of processors
Used to provide coherence across multiple chips in CMP systems (e.g., IBM Power 5)
P
L1
Mem
P
L1
Mem
P
L1
Mem
P
L1
Mem
P
L1
Mem
P
L1
Mem

## Slide 20: Snooping with Ring
CS/ECE 6810 Computer Architecture
How to enforce write serialization in a ring?
Solution: Every address has a home node. If there are two racing writes, ties are broken via the home node. Whatever reaches there first, is said to have serialized first.
P
L1
Mem
P
L1
Mem
P
L1
Mem
P
L1
Mem
P
L1
Mem
P
L1
Mem

## Slide 21: Directory Coherence Protocol
CS/ECE 6810 Computer Architecture
Snooping coherence
  Global state of a memory line is the collection of its state in all caches, and there is no summary state anywhere
  All cache controllers monitor all other caches’ activities and maintain the state of their lines
  Requires a broadcast shared medium (e.g., bus or ring) that also maintains a total order of all transactions
  Bus acts as a serialization point to provide ordering
Directory coherence
  Global state of a memory line is the collection of its state in all caches, but there is a summary state at the directory
  Cache controllers do not observe all activity, but interact only with directory
  Can be implemented on scalable networks, where there is no total order and no simple broadcast, but only one-to-one communication
  Directory acts as a serialization point to provide ordering

## Slide 22: Directory Structure
CS/ECE 6810 Computer Architecture
Directory information (for every memory line)
  Line state bits (e.g., not cached, shared, modified)
  Sharing bit-vector: one bit for each processor that is sharing or for the single processor that has the modified line
  Organized as a table indexed by the memory line address
Directory controller
  Hardware logic that interacts with cache controllers and enforces cache coherence
Sharing vector
0
0
0
0
0
Line state
Memory
4
Cache states:
00 = invalid
01 = shared
10 = modified
Dir. states:
00 = not cached
01 = shared
10 = modified
Directory information
Up to 3 processors can be supported
Line is not cached so sharing vector
is empty and memory value is valid
1
0
1
0
1
9
Line is shared in P0 and P2
and memory value is valid

## Slide 23: Directory Operation
CS/ECE 6810 Computer Architecture
Example: load with no sharers
Sharing vector
0
0
0
0
0
Line state
Memory
4
P0
L1
0
0
Line state
P1
L1
0
0
Line state
P2
L1
0
0
Line state
Cache states:
00 = invalid
01 = shared
10 = modified
Dir. states:
00 = not cached
01 = shared
10 = modified
Load
Miss
1
1
4
Value
1

## Slide 24: Directory Operation
CS/ECE 6810 Computer Architecture
Example: load with sharers
Sharing vector
0
0
1
0
1
Line state
Memory
4
P0
L1
0
1
Line state
P1
L1
0
0
Line state
P2
L1
0
0
Line state
Cache states:
00 = invalid
01 = shared
10 = modified
Dir. states:
00 = not cached
01 = shared
10 = modified
Load
4
Miss
1
4
4
Value
1

## Slide 25: Directory Operation
CS/ECE 6810 Computer Architecture
Example: store with sharers
Sharing vector
0
1
1
0
1
Line state
Memory
4
P0
L1
0
1
Line state
P1
L1
0
1
Line state
P2
L1
0
0
Line state
Cache states:
00 = invalid
01 = shared
10 = modified
Dir. states:
00 = not cached
01 = shared
10 = modified
Store
4
Miss
4
4
0
Acknowledge
6
Acknowledge
1
0
Invalidate
1
0
0
Reply

## Slide 26: Directory Operation
CS/ECE 6810 Computer Architecture
Example: load with owner
Sharing vector
0
1
0
1
0
Line state
Memory
4
P0
L1
0
0
Line state
P1
L1
1
0
Line state
P2
L1
0
0
Line state
Cache states:
00 = invalid
01 = shared
10 = modified
Dir. states:
00 = not cached
01 = shared
10 = modified
Load
4
4
6
Miss
Forward
0
1
6
Value
0
1
Acknowledge+Value
1
0
1
6

## Slide 27: Notes on Directory Operation
CS/ECE 6810 Computer Architecture
On a write with multiple sharers it is necessary to collect and count all the invalidation acknowledgements (ACK) before actually writing
On transactions that involve more complex state changes the directory must also receive acknowledgement
  To establish the completion of the load or store
As with snooping on buses, “the devil is in the details” and we actually need transient states, must deal with conflicting requests, and must handle multi-level caches
As with buses, when buffers overflow we need to introduce NACKs
Directories should work well if only a small number of processors share common data at any given time (otherwise broadcasts are better)

## Slide 28: Quantitative Motivation for Directories
CS/ECE 6810 Computer Architecture
Number of invalidations per store miss on MSI with infinite caches
Bottom-line: number of sharers for read-write data is small
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8to11 | 12to15 | 16to19 | 20to23 | 24to27 | 28to31 | 32to35 | 36to39 | 40to43 | 44to47 | 48to51 | 52to55 | 56to59 | 60to63
LU | 10 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Radix | 28 | 72 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Ocean | 0 | 80 | 15 | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Raytrace | 2 | 72 | 20 | 5 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Barnes-Hut | 2 | 48 | 23 | 10 | 6 | 3 | 1 | 2 | 3 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Radiosity | 6 | 58 | 11 | 5 | 3 | 2 | 1 | 1 | 4 | 3 | 2 | 2 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Culler and Singh
Fig. 8.9

## Slide 29: Example Implementation Difficulties
CS/ECE 6810 Computer Architecture
Operations have to be serialized locally
Operations have to be serialized at directory
P0
P1
Dir.
1. P0 sends read request for line A.
1
2. P1 sends read exclusive (write miss) request for line A (waits at dir.).
2
3. Dir. responds to (1), sets sharing vector (message gets delayed).
3
4a/b. Dir. responds to (2) to both P0 (sharer) and P1 (new owner).
4a
4b
Problem: when (3) finally arrives at P0 the stale value of line A is placed in the cache. Solution: P0 must serialize transactions locally so that it won’t react to 4b while it has a read pending.
5. P0 invalidates line A and sends acknowledgement
5
P0
P1
Dir.
1. P1 sends read excl. request for line A.
1
2. Dir. forwards request to P0 (owner).
2
4. P1 receives (3a) and considers read excl. complete. A replacement miss sends the updated value back to memory.
4
Problem: when (4) arrives dir. accepts and overwrites memory. When (3b) finally arrives dir. completes ownership transfer and thinks that P1 is the owner. Solution: dir. must serialize transactions so that it won’t react to 4 while the ownership transfer is pending.
3b
3a/b. P0 sends data to P1 which forwards to dir. (gets delayed).
3a

## Slide 30: Directory Overhead
CS/ECE 6810 Computer Architecture
Problem: consider a system with 128 processors, 256GB of memory, 1MB L2 cache per processor, and 64byte cache lines
  128 bits for sharing vector plus 3 bits for state → ~16bytes
  Per line: 16/64 = 0.25 → 25% memory overhead
  Total: 0.25*256G = 64GB of memory overhead!
Solution: Cached Directories
  At any given point in time there can be only 128M/64 = 2M lines actually cached in the whole system
  Lines not cached anywhere are implicitly in state “not cached” with null sharing vector
  To maintain only the entries for the actively cached lines we need to keep the tags → 64bits = 8bytes
  Overhead per cached line: (8+16)/64 = 0.375 → 37.5% overhead
  Total overhead: 0.375*128M = 48MB of memory overhead

## Slide 31: Scalability of Directory Information
CS/ECE 6810 Computer Architecture
Problem: number of bits in sharing vector limit the maximum number of processors in the system
  Larger machines are not possible once we decide on the size of the vector
  Smaller machines waste memory
Solution: Limited Pointer Directories
  In practice only a small number of processors share each line at any time
  To keep the ID of up to n processors we need log2n bits and to remember m sharers we need m IDs → m*log2n
  For n=128 and m=4 → 4*log2128 = 28bits = 3.5bytes
  Total overhead: (3.5/64)*256G = 14GB of memory overhead
  Idea:
    Start with pointer scheme
    If more than m processors attempt to share the same line then trap to OS and let OS manage longer lists of sharers
    Maintain one extra bit per directory entry to identify the current representation

## Slide 32: Distributed Directories
CS/ECE 6810 Computer Architecture
Directories can be used with UMA systems, but are more commonly used with NUMA systems
In this case the directory is actually distributed across the system
These machines are then called cc-NUMA, for cache-coherent-NUMA, and DSM, for distributed shared memory
Interconnection
CPU
Cache
Mem.
Node
Dir.
CPU
Cache
Mem.
Dir.
CPU
Cache
Mem.
Dir.
CPU
Cache
Mem.
Dir.

## Slide 33: Combined Coherence Schemes
CS/ECE 6810 Computer Architecture
Use bus-based snooping in nodes and directory (or bus snooping) across nodes
  Bus-based snooping coherence for a small number of processors is relatively strait-forward
  Hopefully communication across processors within a node will not have to go beyond this domain
  Easier to scale up and down the machine size
  Two levels of state:
    Per-node at higher level (e.g., a whole node owns modified data, but Dir. does not know which processor in the node actually has it)
    Per-processor at lower level (e.g., by snooping inside the node we can find the exact owner and the exact up-to-date value)
Bus
CPU
Main memory
CPU
CPU
CPU
Cache
Cache
Cache
Cache
Dir.
Bus or Scalable interconnect
Bus
CPU
Main memory
CPU
CPU
CPU
Cache
Cache
Cache
Cache
Dir.

## Slide 34: Current Trends on Coherence
CS/ECE 6810 Computer Architecture
Open protocol specifications
  CXL: Compute Express Link: cache coherent interconnect for linking different processors (e.g., NICs, GPUs) in a multi-chip multiprocessor
  CHI: cache coherent interconnect for linking different processors within a chip.
  These are all MESI protocol variants at the end of the day.