## Slide 1: HW Support for Shared Memory
Cache Coherence
  Caches + multiprocessers  stale values
  System must behave as if caches are not present
  Cache coherence is implementation that ensures this via:
    Write propagation
    Write serialization
Memory Consistency
  When (in what order) should writes propagate?
  What value should a read return?
  Memory consistency is a specification.
Primitive synchronization instructions
  Certain hardware instructions are extremely useful/required for achieving synchronisation
  Memory fences: memory ordering on demand
  Read-Modify-writes: support for locks (critical sections)
  Transactional memory extensions
CS/ECE 6810 Computer Architecture

## Slide 2: Lect. 5: Memory Consistency
CS/ECE 6810 Computer Architecture
Consider the following code:
  What are the possible outcomes? (assuming caches are coherent)
A=0, B=0, C=0;
…
C = 1;
A = 1;
while (A==0);
B = 1;
P1
P2
initialization
parallel
while (B==0);
print A, C;
P3

## Slide 3: Lect. 5: Memory Consistency
CS/ECE 6810 Computer Architecture
Consider the following code:
A=0, B=0, C=0;
…
C = 1;
A = 1;
while (A==0);
B = 1;
P1
P2
initialization
parallel
A==1, C==1?
A==0, C==1?
A==0, C==0?
A==1, C==0?
while (B==0);
print A, C;
P3
Yes. This is what one would expect.
Yes. If st to B overtakes the st to A on the interconnect toward P3.
Yes. If the st to A overtakes the st to C from the same processor.
Notes: If A = 0 is observable it is a violation of multi-copy atomicity. Why? Because it means that A was observed by P2 but later (in logical time), was not observed by P3.

## Slide 4: Memory Consistency
CS/ECE 6810 Computer Architecture
Cache coherence:
  Makes caches invisible
  But does not guarantee ordering of loads and stores to different addresses in general.
Memory consistency:
  Specifies the ordering of loads and stores to different memory locations
  Defined in so called Memory Consistency Models
  Note that the memory consistency model is part of the ISA specification.
  Languages also have a memory model. Compiler enforces the language memory model leveraging the ISA consistency model.
Cache coherence is a component of memory consistency enforcement. Memory consistency is specification. Cache coherence is part of the implementation.

## Slide 5: Memory Consistency vs Coherence

## Slide 6: Sequential Consistency (SC)
A multiprocessor system is sequentially consistent if the result of any execution is
the same as if the operations of all the processors were executed in some sequential order, and the operations of each individual processor appear in this sequence in the order specified by its program.
[Lamport 78]
CS/ECE 6810 Computer Architecture

## Slide 7: Sequential Consistency (SC)
CS/ECE 6810 Computer Architecture
Key ideas:
  The behaviour should be the same as in a time-shared multiprocessor
  Two aspects:
    Program order: memory ordering has to follow the individual order in each thread
    (RR, RW, WW, WR)
    Write-atomicity: there can be any interleaving of such sequential segments - but a single total order of all memory operations
  Notice that in practice many orderings are still valid
P0
P1
Pn
Memory

## Slide 8: Example: Sequential Consistency
CS/ECE 6810 Computer Architecture
Some valid SC orderings:
A=0, B=0, C=0;
…
C = 1;
A = 1;
while (A==0);
B = 1;
P1
P2
initialization
parallel
P1: st C # C=1
P1: st A # A=1
P2: ld A # while
P2: st B # B=1
P3: ld B # while
P3: ld A # print
while (B==0);
print A;
P3
P1: st C # C=1
P2: ld A # while
…
P1: st A # A=1
P2: ld A # while
P2: st B # B=1
P3: ld B # while
P3: ld A # print
P1: st C # C=1
P2: ld A # while
…
P1: st A # A=1
P2: ld A # while
P3: ld B # while
…
P2: st B # B=1
P3: ld B # while
P3: ld A # print
Notes: With SC, the final print of A will have to print 1.

## Slide 9: Is this ordering SC?
CS/ECE 6810 Computer Architecture
A=0, B=0, C=0;
…
C = 1;
A = 1;
while (A==0);
B = 1;
P1
P2
initialization
parallel
P1: st A # A=1
P1: st C # C=1
P2: ld A # while
P2: st B # B=1
P3: ld B # while
P3: ld A # print
while (B==0);
print A;
P3

## Slide 10: Is this ordering SC? Yes!
CS/ECE 6810 Computer Architecture
A=0, B=0, C=0;
…
C = 1;
A = 1;
while (A==0);
B = 1;
P1
P2
initialization
parallel
P1: st A # A=1
P1: st C # C=1
P2: ld A # while
P2: st B # B=1
P3: ld B # while
P3: ld A # print
while (B==0);
print A;
P3
P1: st C # C=1
P1: st A # A=1
P2: ld A # while
P2: st B # B=1
P3: ld B # while
P3: ld A # print
The values returned by the reads of the execution on the left matches that of the SC execution on the right!

## Slide 11: Terminology
CS/ECE 6810 Computer Architecture
Issue: memory operation leaves the processor and becomes visible to the memory subsystem
Performed: memory operation appears to have taken place
  Performed w.r.t. processor X: as far as processor X can tell
    E.g., a store S by processor Y to variable A is performed w.r.t. processor X if a subsequent load by X to A returns the value of S (or the value of a store later than S, but never a value older than that of S)
    E.g., a load L is performed w.r.t. processor X if all subsequent stores from processor X cannot affect the value returned by L
  Globally performed or complete: performed w.r.t. to all processors
    E.g., a store S by processor Y to variable A is globally performed if any subsequent load by any processor to A returns the value of S
X consistent execution: result of any execution that matches one of the possible total orders (interleavings) as defined by model X
  “Result of an execution”: Values returned by the reads

## Slide 12: Sequential Consistency (SC)
CS/ECE 6810 Computer Architecture
Sufficient conditions
  1. Threads issue memory operations in program order
  2. Before issuing next memory operation threads wait until last issued memory operation completes (i.e., performs w.r.t. all other processors)
  3. A read is allowed to complete only if the matching write (i.e., the one whose value is returned to the read) also completes
Notes:
  Condition 2 guarantees program ordering
  Condition 3 guarantees write atomicity
  These conditions are easily violated in real hardware and compilers (e.g., write buffers in hdw. and ld-st scheduling in compiler)
  In practice necessary conditions may be more relaxed

## Slide 13: Write-Serialization vs Write-Atomicity
// Initially all values are 0.
P1 P2 P3 P4
X= 1 X=2
=X(1) =X(2)
=X(2) =X(1)
P1 P2 P3 P4
X= 1 Y=1
=X(1) =Y(1)
=Y(0) =X(0)
CS/ECE 6810 Computer Architecture
Violation of
Write-serialization
Violation of
Write-atomicity

## Slide 14: How SC can be violated
CS/ECE 6810 Computer Architecture
P1
P2
flag1 = 1
if(flag2 == 0)
{
/* critical*/
}
flag2 = 1
if(flag1 == 0)
{
/* critical*/
}
Initially flag1 = flag2 = 0
If write-buffering is used each processor can buffer the writes
(to flag1 and flag2 resp.) and go ahead with the reads. This will
cause both reads (flag1 and flag2) to return 0, causing both P1 and P2 to enter critical section.

## Slide 15: Efficient SC: In-window Speculation
Using speculation (for optimizing WR, RR)
  The later read can be issued earlier
  But memory operations complete in program order
  If an invalidate is received, speculation squashed and replayed starting from the (later) load
Write-prefetching (for optimizing WW)
  Obtain read-exclusive out-of-order (or in parallel)
  Complete writes in program order.
CS/ECE 6810 Computer Architecture

## Slide 16: Efficient SC: In-window Speculation
P1
ld x
ld y
- Load y allowed to execute before load x
- But they commit in order
- Before load y commits, if address y receives an invalidation message, speculation squashed starting from load y and retried.
CS/ECE 6810 Computer Architecture

## Slide 17: Efficient SC: In-window Speculation
P1
St x
St y
Store x and Store y issued to the directory in parallel, where they execute in parallel (i.e., send invalidations, gather acknowledgements)
But in the cache, the value of x is written and made visisble to other processors before the write to y
CS/ECE 6810 Computer Architecture

## Slide 18: Relaxed Memory Consistency Models
At a high level they relax ordering constraints between pairs of reads, writes, and read-write (e.g., reads are allowed to bypass writes, writes are allowed to bypass each other)
Some of the models also don’t guarantee write atomicity
Some models make synchronization explicit and different from normal loads and stores
Many models have been proposed and implemented
  Total Store Ordering (TSO) (e.g., Sparc, intel): relaxes W—>R ordering
  Partial Store Ordering (PSO) (e.g., Sparc): relaxes W—>R and W —>W
  Relaxed Memory Ordering (RMO) (e.g., Sparc): relaxes all 4 memory orders
  Release Consistency (RC) (e.g RISC-V): relaxes all 4 memory orders but provides release store and acquire load (ARM v8 has a similar model).
  IBM Power/NVIDIA PTX: relaxes all 4 memory orderings; also relaxes write atomicity; provides 2 types of barriers.
    lwsync: ensures R—>R , R—>W, and W—>W; write-atomicity still not ensured
    sync: ensures all 4 memory ordering; write atomicity also ensured.

## Slide 19: Relaxed Memory Consistency Models
CS/ECE 6810 Computer Architecture
Note that every relaxed consistency model ensure single-thread dependencies.
  P1
  X = 2
  r1 = X
  (r1 always reads 1 irrespective of the memory model)

## Slide 20: Relaxed Memory Consistency Models
CS/ECE 6810 Computer Architecture
  Whether these single threaded dependencies induce a global ordering is a different matter!!!
  Relaxed memory models have complex rules regarding that!
  We will come back to this in a couple of slides

## Slide 21: Example: Total Store Ordering (TSO)
CS/ECE 6810 Computer Architecture
Reads are allowed to bypass writes (can hide write latency)
Still makes prior example work as expected,
but breaks some intuitive assumptions,
…
data = 1;
flag = 1;
while (flag==0);
Print data;
P1
P2
…
A = 1;
Print B;
B = 1;
Print A;
P1
P2
SC guarantees that A==0 and B==0 will never be printed
TSO allows it if ld B (P1) overtakes st A (P1) and ld A (P2) overtakes st B (P2)

## Slide 22: TSO Examples
CS/ECE 6810 Computer Architecture
  //Initially x = 0
  P1.
  X = 1
  r1 = X
  Can r1 ever be 0? No!
  //Initially X = Y =0
  P1. P2
  X =1. Y = 1
  r1 = X r3 = Y
  r2 = Y. r4 = X
  What values do r1 and r3 read? (they have to read 1)
  Can both r2 and r4 = 0? (Yes, according to TSO)

## Slide 23: Example: Release Consistency (RC)
CS/ECE 6810 Computer Architecture
Reads and writes are allowed to bypass both reads and writes (i.e., any order that satisfies control flow and data flow is allowed)
Assumes explicit synchronization operations: acquire and release So, for correct operation, our example must become:
Constraints
  All previous writes (and previous reads) must complete before a release can complete
  No subsequent reads (and subsequent writes) can complete before a previous acquire completes
  All synchronization operations must be sequentially consistent (i.e., follow the rules for SC, where an acquire is equivalent to a read and a release is equivalent to a write)
…
data = 1;
Release:flag=1;
Acquire:while (!flag);
Print data;
P1
P2

## Slide 24: Example: Release Consistency (RC)
CS/ECE 6810 Computer Architecture
Example: original program order
Read/write
…
Read/write
P1
Acquire
Read/write
…
Read/write
Release
Read/write
…
Read/write
Allowable overlaps
  Reads and writes from block 1 can appear after the acquire
  Reads and writes from block 3 can appear before the release
  Between acquire and release any order is valid in block 2 (and also 1 and 3)
Note that despite the many reorderings, this still matches our intuition of critical sections
1
2
3
Read/write
…
Read/write
1
Acquire
Read/write
…
Read/write
Release
2
Read/write
…
Read/write
3

## Slide 25: RC example: control dependency.
CS/ECE 6810 Computer Architecture
  //Initially X = Y =0
  P1. P2
  X =1. r1 = Y//reads 1
  Rel Y = 1 if(r1 ==1)
  r2 = X //reads 0?

## Slide 26: RC example: control dependency.
CS/ECE 6810 Computer Architecture
  //Initially X = Y =0
  P1. P2
  X =1. r1 = Y//reads 1
  Rel Y = 1 if(r1 ==1)
  r2 = X //reads 0?
  Possible with RISC-V and ARM!!!

## Slide 27: RC example: address dependency.
CS/ECE 6810 Computer Architecture
  //Initially X = Y =0, assume address of X = 0xffff
  P1. P2
  X =1. r1 = Y. //
  Rel Y = 0xffff r2 = *(r1) // reads 0?

## Slide 28: RC example: address dependency.
CS/ECE 6810 Computer Architecture
  //Initially X = Y =0, assume address of X = 0xffff
  P1. P2
  X =1. r1 = Y. //
  Rel Y = 0xffff r2 = *(r1) // reads 0?
  No, according to RISC-V and ARM!

## Slide 29: Implementing RC
RC with writer-initiated invalidations:
  Writes retire into write buffer (and could complete out of order)
  Reads maybe be issued out-of-order (and may complete out of order, although in practice they processors commit in order.)
  Note: Invalidates need not snoop LSQ
  A release drains the write-buffer
  All loads following an acquire are issued after the acquire.
Question: Must writes invalidate shared copies?
CS/ECE 6810 Computer Architecture

## Slide 30: Implementing RC
Writes without writer-initiated invalidations
  Writes retire into write buffer
    (and complete out of order)
    But only written to the local cache – no eager invalidates.
  A release writes all dirty blocks (including the release write) in the local cache into coherent lower-level cache (memory)
  Reads maybe be issued out-of-order (but completed in inorder)
  Upon an acquire the acquire load is forced to miss the local cache and then all valid blocks self-invalidated
CS/ECE 6810 Computer Architecture

## Slide 31: Implementing RC
CS/ECE 6810 Computer Architecture
…
data = 1;
Release:flag=1;
Acquire:while (!flag);
Print data;
P1
P2
Upon release, write buffer flushed to lower level cache
Upon acquire, local cache invalidated

## Slide 32: RC using self-invalidations:
Does not require a sharer vector
Would still benefit from local/shared tracking
  Local data need not be written to the lower-level upon a release
  Local data need not be self-invalidated upon an acquire
  Could use the directory to track this or even the TLB. (How)?
Aside: Is the cache still coherent?
CS/ECE 6810 Computer Architecture

## Slide 33: RC using self-invalidations:
Does not require a sharer vector
Would still benefit from local/shared tracking
  Local data need not be written to the lower-level upon a release
  Local data need not be self-invalidated upon an acquire
  Could use the directory to track this or even the TLB. (How)?
Aside: Is the cache still coherent?
  Yes: guarantees write serialization and write propagation
CS/ECE 6810 Computer Architecture

## Slide 34: Do consistency models matter?
Not a lot of people write parallel programs using assembly!
  Use synchronization libraries mainly: locks, barriers etc.
Matters to expert programmers though who want performance
  Systems programmers (OS writers, compiler writers)
  Certain application programmers
Even they don’t program in assembly – Languages have consistency models

## Slide 35: Language based consistency models
Abstraction over the ISA
Typically, a relaxed consistency model – a variant of release consistency
  Release, acquire, different types of fences and RMWs
  Lack store atomicity
Compiler implements the language model
One problem: the “out of thin air problem”

## Slide 36: Out of Thin Air
Initially X = Y = 0
P1 P2
r1 = X r2 = Y
Y = r1 X = r2
Can r1 = r2 = 42?
Notes: Languages specification might allow this. Why?
Ld  St ordering is not enforced.
Compiler might speculate the first load reads 42, then store Y=42, and after operations from P2 have performed, the prediction becomes true.

## Slide 37: Out of Thin Air
Initially X = Y = 0
P1 P2
r1 = X r2 = Y
Y = r1 X = r2
Can r1 = r2 = 42?
Notes: Note that this litmus test result should be allowed, and is allowed by some hardware : e.g., Power.

## Slide 38: But wait…why don’t ISA memory model have this problem?
Because none of the hardware models allow this
Initially X = Y = 0
P1 P2
r1 = X r2 = Y
Y = r1 X = r2
Can r1 = r2 = 42? No!
Notes: Because hardware memory models honor syntactic dependencies. The moment there is a syntactic dependency between a load and store the two operations are ordered.

## Slide 39: Case study: RISC-V memory model
https://courses.cs.washington.edu/courses/csep551/19au/readings/riscv-base.pdf

## Slide 40: Case-study: RISC-V memory model

## Slide 41: Case-study: RISC-V memory model